## nmcli (NetworkManager CLI)
### Quick Commands
View current connections:
nmcli connection show

View device information from all devices:
nmcli device show

### Add new interface with static IP
First get the name of the interface:
ip a

Then add a new connection:
nmcli connection add con-name <name-of-connection> ifname <interface-name> type ethernet

This can then look like this: nmcli connection add con-name Connection2 ifname ens19 type ethernet
Enable auto connection:
nmcli connection modify <name-of-connection> connection.autoconnect yes

Set IP:
nmcli connection modify <name-of-connection> ipv4.addresses <ip-with-netmask>

This can then look like this: nmcli connection modify Connection1 ipv4.addresses 192.168.0.2/24
Set method to static:
nmcli connection modify <name-of-connection> ipv4.method static

Set default gateway:
nmcli connection modify <name-of-connection> ipv4.gateway 192.168.0.1

Set DNS server:
nmcli connection modify <name-of-connection> ipv4.dns "192.168.0.1"

Then verify everything was saved correctly:
nmcli device show

If everything is correct, start the new connection:
nmcli connection up <name-of-connection>