## Set Static IP Address / Static route
### ifupdown2
First install the ifupdown2 package:
sudo apt install ifupdown2

It will generate the file /etc/network/interfaces if it doesn't exist.
Then edit /etc/network/interfaces and add the following:
auto eth0 iface eth0 inet static address 172.16.1.20/24 gateway 172.16.1.1 nameserver 172.16.1.1

Adjust the interface name, here eth0, to your configuration.
Finally enable the interface by running:
ifup eth0

Sourced from wiki.debian.org/NetworkConfiguration
### Static route
To show static routes:
ip route

To add a static route run:
ip route add <network>/<netmask> via <gateway>

Example: ip route add 10.205.0.0/24 gw 10.0.0.3
### Static route for LXC
To add a persistent static route for a Linux Container add the following line to the interface that should automatically add the route in /etc/network/interfaces:
up route add -net <network>/<netmask> gw <gateway-ip>

Example: up route add -net 10.205.0.0/24 gw 10.0.0.3
→ tested with a Proxmox CT
Sourced from forum.proxmox.com LXC Container and static route